ANALYTICAL & CONSULTING SERVICES, INC.

www.acslab.net

205 Sergeant Square Drive                                      Sergeant Bluff, IA  51054

Phone:  712-943-4888                      Fax: 712-943-4889           Cell:  712-253-1254         Email: sfranco@acslab.net

Sampling Instructions

IMPORTANT!  Some samples must be analyzed as soon as possible after collection.  Coordinate sampling and delivery time with laboratory so lab can be prepared to analyze samples as soon as possible after receipt.  Freeze all ice packs or fill ice bags and return them in the cooler with the sample(s).

Review sampling procedure below and contact laboratory prior to sampling with any questions.  Contact numbers and email are listed above.

Sampling Procedure

- Collect samples in the clean bottles supplied by the lab or use clean.

- Fill bottles to within ½ inch from the top.

- Samples may be grab samples or composite samples; however, sample type may be specified in your permit if sampling is done for compliance purposes.  For a grab sample, collect a representative grab sample from the water to be tested.  For a composite sample, keep the temperature of the sample at or below 4oC while compositing.

- CAUTION!  Some bottles contain preservatives (H2SO4, NaOH, HNO3), therefore do not overfill bottle and do not rinse bottle out.

- Refrigerate samples until they will be brought or shipped to the lab.

- Place frozen ice packs or ice bags and samples back in cooler.

- Return samples and cooler to lab.